Doc #: 1107-0000		Client Name: New Homeowner

Dwelling Address:  2400 Anywhere Ave		Inspector:  Donald C. Bedner

Any town, NC 27000		Client's Agent: Susan Best

This summary is provided to highlight those findings that we believe are significant in nature and which evidence suggest are in immediate need of repair. These findings are also listed in the full report on the following pages. Photographs are provided of selected items to enhance client understanding. Not all items on this summary will have photographs. The full report also outlines more minor findings as well as comments regarding routine maintenance. This summary does not limit your ability to use the entire report in completing your transaction.

The NC Home Inspection Licensure Board has established the Summary Report to identify items which meet one of the following criteria. The system or component:

1. Does not function as intended.

2. Adversely affects the habitability of the dwelling.

3. Warrants further investigation by a specialist.

4. Requires subsequent observation.

THIS SUMMARY IS NOT THE ENTIRE REPORT. THE FULL REPORT MAY INCLUDE ADDITIONAL INFORMATION OF INTEREST OR CONCERN TO THE CLIENT. IT IS STRONGLY RECOMMENDED THAT THE CLIENT PROMPTLY READ THE COMPLETE REPORT. FOR INFORMATION REGARDING THE NEGOTIABILITY OF ANY ITEM IN THIS REPORT UNDER A REAL ESTATE PURCHASE CONTRACT, CONTACT YOUR NORTH CAROLINA REAL ESTATE AGENT OR AN ATTORNEY.

EXTERIOR

| 1104 | Exterior Wall Cladding | Recommendation. Brick, vinyl. Settlement cracking observed at left side and left rear below master bedroom. Recommend sealing open joints to prevent water entry. It is not possible to determine the rate of movement during this inspection. Recommend evaluation by a Structural Engineer or Licensed General Contractor with foundation settlement experience for repairs as needed. |
| --- | --- | --- |
| 1106 | Windows & Frames | Recommendation. Wood double hung, fixed. Metal storms. Open joints observed between windows and bricks. Recommend sealing open joints to prevent water entry. Cracked/damaged storm window at left side bedroom. Recommend maintenance/repair by a Licensed General Contractor. |
| 1110 | Outside Faucet - Hose bib | Recommendation. Front and rear. Leaking faucet noted at front. Sometimes this is visible only under pressure. Recommend repair by a Licensed Plumber. |
| 1112 | Bell/Chime | Recommendation. Door bell inoperable at front. Recommend maintenance/repair by a Licensed Electrician. |
| 1113 | Exterior Doors | Recommendation. Rear storm door will not close properly. Adjustments needed for proper operation. Damaged door at utility and door will not latch. Recommend maintenance/repair by a Licensed General Contractor. |

ATTIC

| 1401 | Access | Recommendation. Loose bolts and nuts noted. Recommend maintenance/repair by a Qualified Specialist. |
| --- | --- | --- |
| 1405 | Ventilation | Recommendation. Master bath vent fan exhausts into attic. Recommend extending vent exhaust to exterior to prevent moisture damage in attic area. Recommend maintenance/repair by a Qualified Specialist. |

GARAGE -DETACHED

| 1502 | Exterior | Recommendation. Vinyl. Damaged siding noted at left side (facing from street) panel and vinyl corner trim. Siding to ground contact at rear. Recommend changing grade to prevent damage behind siding. |
| --- | --- | --- |
| 1507 | Garage Door Opener | Recommendation. This garage door is equipped with an electric eye safety reverse device and a manual safety reverse device. The U.S. Product Safety Commission recommends that these devices be checked monthly for proper operation and safety. The door would not close properly and retracted indicating electric eyes are not functioning properly. Recommend maintenance/repair by a Qualified Specialist. |
| 1515 | Electrical | Recommendation. Exposed wires noted at rear outlet. Exposed wires should be covered for safety. Recommend maintenance/repair by a Licensed Electrician. |

CRAWLSPACE

| 1805 | Floor Joists | Recommendation. 2 x 10. Some Mold noted on joists at center rear and center front. This is an indication that joists have been wet or the crawlspace environment is damp. Client should keep crawlspace vents open to maximize ventilation. Recommend annual review to ensure crawlspace remains dry and the current mold growth is not increasing. If client is concerned suggest review by a qualified specialist |
| --- | --- | --- |
| 1810 | Insulation | Recommendation. Rolled fiberglass insulation approximately 4-6 inches. Insulation is missing, loose and hanging down at several locations. Recommend re-installing by a Qualified Specialist. |
| 1818 | Crawlspace Comments | Recommendation. Wood scraps noted at several locations throughout crawlspace. Recommend removing all wood scraps and debris from crawlspace. |

ELECTRICALSYSTEM

| 2102 | Additional Main Panel Comments | Recommendation. Double lugging noted at exterior rear panel left side 30 amp breaker. This can add to the load of the affected circuits causing a possible overload and tripping of the breakers. This is a safety concern. Damaged/loose hinges on exterior panel. Recommend review by a Licensed Electrician for repairs as needed to ensure safety. |
| --- | --- | --- |
| 2104 | Smoke Detectors | Recommendation. Smoke detector(s) located at hall. Smoke detector inoperable at hall. Recommend replacing smoke detector. |

KITCHEN/BREAKFAST

| 2311 | Faucets | Recommendation. Hand Sprayer leaks. Recommend replacing hand sprayer to prevent damage under sink. Recommend maintenance/repair by Licensed Plumber. |
| --- | --- | --- |
| 2314 | Dishwasher | Recommendation. Appliance Brand: Kenmore. Grinding noise noted at startup of pump. Unit is not secured to cabinet. Recommend maintenance/repair by a Qualified Specialist. |
| 2315 | Stove/Cook Top/Oven | Recommendation. Electric. Appliance Brand Kenmore. Unit is not secured with an anti tip device. This may not have been required at time of installation. Recommend Qualified Specialist install anti tip device for safety. |
| 2316 | Oven-Separate Unit | Recommendation. Appliance Brand: GE. Oven bake element would not heat properly. Recommend maintenance/repair by a Qualified Specialist. |

INTERIORS

| 2351 | Comments | Recommendation. Several Baseboard electrical heat units /thermostats throughout home are inoperable/or disconnected. Recommend review of all baseboard heat by a Licensed Electrician if client plans on using this system. |
| --- | --- | --- |

FAMILY ROOM

| 2604 | Doors | Recommendation. Door is loose and will not latch to hall. Recommend maintenance/repair by a Licensed General Contractor. |
| --- | --- | --- |

BATHROOM – MASTER

| 3004 | Doors | Recommendation. Door will not latch. Recommend maintenance/repair by a Licensed General Contractor. |
| --- | --- | --- |

BATHROOM – HALL

| 3010.2 | Tub/Surround | Recommendation. Porcelain tub and tile. Cracked caulk and grout was noted. Recommend all tile edges and tub/shower walls be caulked and sealed to prevent moisture penetration. All damaged caulk and grouting should be replaced. Failure to keep walls sealed can cause deterioration and extensive moisture damage to the interior walls and sub-flooring. This damage is not always visible or accessible to the inspector at the time of inspection. |
| --- | --- | --- |
| 3018.2 | Traps/Drain Supply | Recommendation. Tub drains slowly. Recommend maintenance/repair by a Licensed Plumber. |

BEDROOM – CENTER FRONT

| 3205.2 | Windows | Recommendation. Locking hardware inoperable. Recommend repairs as needed by a Licensed General Contractor to secure window. . |
| --- | --- | --- |

BEDROOM – LEFT FRONT

| 3205.3 | Windows | Recommendation. Top sash drops at front. Recommend repairs as needed by a Licensed General Contractor |
| --- | --- | --- |

Doc #: 	1107-0000	Inspector: 	Donald C. Bedner

Date: 	6/20/2011

Dwelling Address: 	2400 Anywhere Ave.

Any town, NC 27000

Client Name: 	New Homeowner

Client's Agent: 	Susan Best	 	Real Estate Company: Best Realty.

GENERAL INFORMATION

A certified home inspector from NC-Choice Home Inspection Service prepared this report.  Please read the report completely and if you have questions, contact the inspector at the phone number or address printed above.

This report is designed to comply with the standards established by The North Carolina Home Inspection Licensure Board, the International Association of Home Inspectors, Inter NACHI and NC-Choice, Inc., Browns Summit, North Carolina. A copy of the North Carolina Home Inspection Standards of Practice and Code of Ethics may be obtained by writing the Board at 1202 Mail Service Center, Raleigh, NC 27699-1202. As stated in your inspection agreement, this inspection is limited to visible and accessible components only. Examination of concealed or inaccessible portions of the property is beyond the scope of this inspection.

You are also advised to perform your own walk through of the property just prior to closing to ensure that all components are in good working order and that agreed-upon repairs have been performed properly. If possible, obtain repair receipts from the seller at or prior to closing. Your NC-Choice inspector is available to perform a re-inspection of repaired items. An additional fee is charged for this service. Not all conditions may become apparent at the time of inspection. For that reason, it is recommended that you obtain a Home Warranty Plan.

DEFINITION OF TERMS

The following information is provided to assist you in using this report. Please read the entire report to facilitate your understanding of this property.

Serviceable-The materials and workmanship are acceptable and in generally satisfactory condition. We will occasionally point out a minor item and still note Serviceable, such as a light fixture with no globe.

None-The item does not apply to this property.

Recommendation-Recommend is used to indicate when the inspector's evaluation leads him to believe action should be taken to address the item.

Suggestion-Suggest is used to indicate items the client may choose to address in the future to maintain upgrade and/or improve the property.

GENERAL CONDITIONS

MAJOR SYSTEMS - Our evaluation of major systems is both visual and functional provided power and/or fuel is supplied to the component.  Identifying or testing for the presence of asbestos, radon, lead based products or other potentially hazardous materials is not within the scope of this report.  Judging the sufficiency of water flow in plumbing or the cooling efficiency of air conditioning is a subjective evaluation, therefore, we only note a poor condition if, in the inspector's opinion, the adequacy seems to be less than normal.  We urge you to evaluate these systems prior to closing.  DISMANTLING AND/OR EXTENSIVE INSPECTION OF INTERNAL COMPONENTS OF ANY APPLIANCE, INCLUDING HEATERS AND HEAT EXCHANGERS, IS BEYOND THE SCOPE OF THIS REPORT.  THE LOCAL UTILITY COMPANY MAY CONDUCT SUCH AN INSPECTION UPON REQUEST.

INTERIOR - Our review of interior rooms is visual and evaluated with similar aged homes in mind.  Cosmetic considerations and minor flaws such as a torn screen or an occasional cracked window may not always be reported.

MOLD - Your home inspection report may note the presence of mold, mildew, or fungus, on visible surfaces, however, even if mold, mildew, or fungus were undetected, they may become visible in the future, with the right conditions, or they may be lying in inaccessible areas, such as wall cavities or under floor coverings. Any time we note the presence of staining and/or a mold or mildew condition we suggest maintenance be performed to correct the condition. We are not industrial hygienists and therefore lack the qualifications or ability to evaluate the mold to determine if it may carry any health risks. Should you have concerns regarding mold we suggest review by a qualified professional.

INTERIOR - Our review of interior rooms is visual and evaluated with similar aged homes in mind.  Cosmetic considerations and minor flaws such as a torn screen or an occasional cracked window may not always be reported.

MOLD - Your home inspection report may note the presence of mold, mildew, or fungus, on visible surfaces, however, even if mold, mildew, or fungus were undetected, they may become visible in the future, with the right conditions, or they may be lying in inaccessible areas, such as wall cavities or under floor coverings. Any time we note the presence of staining and/or a mold or mildew condition we suggest maintenance be performed to correct the condition. We are not industrial hygienists and therefore lack the qualifications or ability to evaluate the mold to determine if it may carry any health risks. Should you have concerns regarding mold we suggest review by a qualified professional.

| 1001 | INSPECTOR | Donald Bedner, Inspector, NC License #2291. |
| --- | --- | --- |
| 1002 | CLIENT | Buyer. This confidential home inspection report has been prepared for the exclusive use of the buyer. Any use by unauthorized persons is prohibited. |
| 1003 | STRUCTURE TYPE | Single family wood frame, brick veneer. |
| 1004 | LEVELS | 1 story structure. Brick veneer. |
| 1005 | ESTIMATED AGE | Estimated construction date is 1966. |
| 1006 | WEATHER CONDITIONS | Clear. Hot. Temperature at time of inspection 92F. |
| 1007 | OCCUPANT STATUS | Owner occupied. |
| 1008 | ATTENDING INSPECTION | Buyer & Buyer's Agent. |
| 1009 | START/STOP TIME | Approximate inspection start time was 12:15pm and inspection was completed at 4:15pm. |

EXTERIOR

Our exterior evaluation is visual in nature and is based on our experience and understanding of common building methods and materials. Our review does not take into consideration the normal wear associated with virtually all properties. Hairline cracks in stucco, concrete, asphalt, plaster and drywall are common and are not a significant defect unless otherwise stated. The exterior wall cavities are typically not accessible and cannot be reviewed. The presence, absence and/or condition of screens are not within the scope of the inspection. If screens are a concern to the client, all screens should be reviewed prior to closing.

| Step # | Component | Comments |
| --- | --- | --- |
| 1101 | Driveway | Serviceable. Concrete. Common cracks noted. |
| 1102 | Walkways | Serviceable. Concrete, concrete stepping stones. |
| 1103 | Fences/Gates | None. |
| 1104 | Exterior Wall Cladding | Recommendation. Brick, vinyl. Settlement cracking observed at left side and left rear below master bedroom. Recommend sealing open joints to prevent water entry. It is not possible to determine the rate of movement during this inspection. Recommend evaluation by a Structural Engineer or Licensed General Contractor with foundation settlement experience for repairs as needed. |
| 1105 | Trim | Serviceable. Wood, vinyl, metal. When metal wrap is installed over wood trim no review of the wood behind the wrap is possible. Caulked joints should be maintained to prevent water entry and ensure continued serviceability. |
| 1106 | Windows & Frames | Recommendation. Wood double hung, fixed. Metal storms. Open joints observed between windows and bricks. Recommend sealing open joints to prevent water entry. Cracked/damaged storm window at left side bedroom. Recommend maintenance/repair by a Licensed General Contractor |
| 1107 | Vegetation | Serviceable. Plants and shrubs are placed and trimmed to allow free air flow to help prevent moisture damage to the structure. |
| 1108 | Electrical Fixtures | Suggestion. No ground fault circuit interrupter (GFCI) noted. GFCI protection not required when home was built. GFCI is a safety device that the buyer may wish to install. |
| 1109 | Gutters & Downspouts | Serviceable. Aluminum. The fascia and soffit boards behind and near gutters are not totally accessible. Client is advised that this is a limited review of these areas. Unless noted otherwise in this section evidence suggests these areas are functioning as intended. |
| 1110 | Outside Faucet - Hose bib | Recommendation. Front and rear. Leaking faucet noted at front. Sometimes this is visible only under pressure. Recommend repair by a Licensed Plumber. |
| 1111 | Sprinkler System | None. |
| 1112 | Bell/Chime | Recommendation. Door bell inoperable at front. Recommend maintenance/repair by a Licensed Electrician. |
| 1113 | Exterior Doors | Recommendation. Rear storm door will not close properly. Adjustments needed for proper operation. Damaged door at utility and door will not latch. Recommend maintenance/repair by a Licensed General Contractor. |
| 1114 | Chimney | Serviceable. The chimney review is limited to the visible/accessible components only. Examination of concealed/inaccessible portions of the chimney is beyond the scope of this inspection. This includes determining the presence of a flue lining, or if lining is present, checking for deterioration, damage or cracks. This was a limited inspection. If further review is desired, client is advised to consult with a qualified Licensed Contractor prior to closing. Spark arrester noted for safety. |
| 1115 | Lot/Grade Drainage | Serviceable. Sloped lot. Water seepage and moisture penetration are common problems in basements and crawlspaces usually resulting from inadequate water management above ground. Improving drainage and grading can correct most causes. All soil should slope away from the foundation wall and all gutter downspouts should carry water away from the foundation wall. NOTE: The presence of a sump pump can suggest water has or may enter the basement or crawlspace. Moisture in a basement or crawlspace can promote wood decay, therefore basements should be kept dry and crawlspaces should be adequately ventilated and vents should be left open year round. Recommend re-grading and adding dirt backfill to any low-lying areas adjacent to the foundation to ensure proper drainage away from the foundation at all times. |
| 1116 | Gas Meter | Serviceable. Rear. |
| 1117 | Exposed Foundation | Serviceable. Brick. |
| 1118 | Exterior Comments | None. |

PATIO/PORCH/BALCONY/AREA WAYS FRONT PORCH

| Step # | Component | Comments |
| --- | --- | --- |
| 1201 | Location/Type | Front Porch. |
| 1202 | Cover | Serviceable. Wood. |
| 1203 | Enclosure | None. |
| 1204 | Electrical | Serviceable. No outlet noted. |
| 1205 | Windows | None. |
| 1206 | Deck/Slab | Serviceable. Concrete, brick. |
| 1207 | Stairs/Stoops | Serviceable. |
| 1208 | Railing | None. |
| 1209 | Ceiling Fan | None. |
| 1210 | Comments | None. |

PATIO/PORCH/BALCONY/AREA WAYS #2 REAR STOOP/PATIO

| Step # | Component | Comments |
| --- | --- | --- |
| 1201.2 | Location/Type | Rear Stoop, patio. |
| 1202.2 | Cover | None. |
| 1203.2 | Enclosure | None. |
| 1204.2 | Electrical | Suggestion. No ground fault circuit interrupter (GFCI) noted. GFCI protection not required when home was built. GFCI is a safety device that the buyer may wish to install. |
| 1205.2 | Windows | None. |
| 1206.2 | Deck/Slab | Suggestion. Brick, concrete. Common cracks noted. Suggest sealing cracks for continued serviceability. . |
| 1207.2 | Stairs/Stoops | Serviceable. |
| 1208.2 | Railing | None. |
| 1209.2 | Ceiling Fan | None. |
| 1210.2 | Comments | None. |

ROOF-Main Structure

Our evaluation of the roof is to determine if portions are missing and/or deteriorating. Portions of underlayment and decking are hidden from view and cannot be evaluated by our visual inspection.  Leaks are not always visible to the inspector, nor can the inspector determine the water-tight integrity of a roof by visual inspection.  If such a review is desired, client should contact a qualified Licensed Roofing Contractor.

| Step # | Component | Comments |
| --- | --- | --- |
| 1301 | Roofing Type & Materials | Sloped asphalt composition shingle. Observed from roof. |
| 1302 | Flashings | Serviceable. |
| 1303 | Conditions | Roof shows normal wear for its age and type. No damaged, deteriorated, or missing roofing materials were noted; evidence suggests roof is functioning properly. This is a VISUAL inspection only. No certification, warranty or guarantee is given as to the water tight integrity of the roof. Inspectors cannot determine the water tight integrity of roofs by a visual inspection nor can they predict future leaks or if installed according to manufacturer's specifications. If such an inspection or certification of the roof is desired, client should contact a qualified Licensed Roofer prior to closing. |
| 1304 | Skylights | None. |
| 1305 | Roof Penetrations | Serviceable. |
| 1306 | Roof Comments | None. |

ROOF-Detached Structure

| Step # | Component | Comments |
| --- | --- | --- |
| 1311 | Roofing Type & Materials | Sloped asphalt composition shingle. Observed from roof. |
| 1312 | Flashings | Serviceable. |
| 1313 | Conditions | Roof shows normal wear for its age and type. No damaged, deteriorated, or missing roofing materials were noted; evidence suggests roof is functioning properly. This is a VISUAL inspection only. No certification, warranty or guarantee is given as to the water tight integrity of the roof. Inspectors cannot determine the water tight integrity of roofs by a visual inspection nor can they predict future leaks or if installed according to manufacturer's specifications. If such an inspection or certification of the roof is desired, client should contact a qualified Licensed Roofer prior to closing. |
| 1314 | Skylights | None. |
| 1315 | Roof Penetrations | None. |
| 1316 | Roof Comments | None. |

ATTIC

The attic review is visual with the attic being entered if safely possible. The attic area was inspected using a standard flashlight and a small probe. Water stains around roof penetrations such as chimneys, plumbing, vents, and heating vents are very common. It is difficult to determine if these stains are active. Insulation in the attic is one of the best ways to improve the energy efficiency of a home. Our report measures insulation materials by thickness. When insulation thickness is less than currently required a suggestion to add insulation is typically made. Generally, the greater the thickness the more resistance there is to heat loss.

| Step # | Component | Comments |
| --- | --- | --- |
| 1401 | Access | Recommendation. Attic access provided by pull down stairs at hall. Attic was accessed unless noted otherwise in this section. Loose bolts and nuts noted. Recommend maintenance/repair by a Qualified Specialist. |
| 1402 | Framing | Serviceable. Trusses, Rafters. |
| 1403 | Sheathing | Serviceable. Plywood. |
| 1404 | Insulation | Suggestion. Blown-in fiberglass insulation approximately 5-7 inches. The insulation does not provide the currently recommended thermal resistance. Suggest adding additional insulation to increase the energy efficiency of this home. |
| 1405 | Ventilation | Recommendation. Gable vents, soffit vents, whole house fan and hooded roof vents. Master bath vent fan exhausts into attic. Recommend extending vent exhaust to exterior to prevent moisture damage in attic area. Recommend maintenance/repair by a Qualified Specialist. |
| 1406 | Electrical | Serviceable. |
| 1407 | HVAC Ducts | Serviceable. |
| 1408 | Duct Insulation | Serviceable. |
| 1409 | Windows | None. |
| 1410 | Attic Comments | None. |

GARAGE - Detached

Our garage/carport evaluation is visual in nature and is based on our experience and understanding of common building methods and materials.  Our review does not take into consideration the normal wear associated with virtually all properties.  Exterior surfaces should be kept well painted, stained or sealed to prevent deterioration. Garage floors should not be covered with carpet, cardboard, wood or other combustible materials and, of course, flammable products should be properly stored. It is recommended all garage door openers be equipped with a regularly tested safety reverse device to reduce chances of injury. Attached garages should be separated from the house by a steel or solid wood door, and common walls should have a fully sealed fire resistant covering such as drywall to protect against fume entry and to slow the migration of smoke or fire from entering the house in the event of a garage fire. Mounting a self-closer on the door between the garage and the house is an additional suggested safety upgrade. We suggest you keep attic hatches closed, repair any holes or damage that exist or occur, and avoid creating openings between the home and garage. It is especially important to keep garage wall and ceiling areas directly beneath living space intact.

| Step # | Component | Comments |
| --- | --- | --- |
| 1501 | Location | Detached. |
| 1502 | Exterior | Recommendation. Vinyl. Damaged siding noted at left side (facing from street) panel and vinyl corner trim. Siding to ground contact at rear. Recommend changing grade to prevent damage behind siding. |
| 1503 | Roof | Garage is detached. See Roof Section at detached structure for more information. |
| 1504 | Floor/Slab | Serviceable. Concrete. |
| 1505 | Garage Door | Serviceable. Wood. |
| 1506 | Garage Door Hardware | Serviceable. Serviceable. |
| 1507 | Garage Door Opener | Recommendation. This garage door is equipped with an electric eye safety reverse device and a manual safety reverse device. The U.S. Product Safety Commission recommends that these devices be checked monthly for proper operation and safety. The door would not close properly and retracted indicating electric eyes are not functioning properly. Recommend maintenance/repair by a Qualified Specialist. |
| 1508 | Windows | Serviceable. |
| 1509 | Fire Door | None. |
| 1510 | Service Door | Serviceable. |
| 1511 | Fire Barrier Wall/Ceiling | None. |
| 1512 | Garage Framing & Supports | Serviceable. |
| 1513 | Walls | Serviceable. |
| 1514 | Ceiling | Serviceable. |
| 1515 | Electrical | Recommendation. Ground fault circuit interrupter (GFCI) noted. Light fixture at ceiling inoperable at several locations. Possible spent bulbs. Switch function at rear unknown. Suggest review with owner. Exposed wires noted at rear outlet. Exposed wires should be covered for safety. Recommend maintenance/repair by a Licensed Electrician. |
| 1516 | Garage Comments | Suggestion. Very limited review due to storage items, moving boxes and furniture items. Suggest review of area after items are removed. |

LAUNDRY AREA

The operation of washers and dryers are not within the scope of this inspection. If these appliances are a part of the clients purchase we suggest the client verify operation with owners prior to closing.

| Step # | Component | Comments |
| --- | --- | --- |
| 1600 | Location | Laundry area is located at kitchen. |
| 1601 | Floor | Serviceable. Vinyl. |
| 1602 | Walls & Ceiling | Serviceable. Painted. |
| 1604 | Doors | Serviceable. |
| 1605 | Windows | None. |
| 1606 | Electrical | Serviceable. |
| 1607 | Heat Source | Suggestion. Electrical Baseboard unit observed. See item 2351 at interiors for additional information. |
| 1608 | Cabinets | None. |
| 1609 | Laundry Sink/Tub | None. |
| 1610 | Washer Hook-ups | Suggestion. The supply hoses to the washer are not disconnected during the inspection, nor do we operate the valves. These can leak at any time and should be considered part of normal maintenance. No test was performed on the washer drain line to determine if the line is draining properly. This was a visual inspection of this area only. No guarantee, warranty, or certification is given as to the future draining capabilities, as drain lines can become blocked at any time without warning. Suggest installing pan under washer to prevent damage to floor to prevent damage to floor should leak occur. . |
| 1611 | Dryer Hook-ups | Suggestion. Electric 240 volt. Suggest cleaning dryer vent as needed for safety. . |
| 1612 | Laundry Area Comments | None. |

UTILITY ROOM

| Step # | Component | Comments |
| --- | --- | --- |
| 1650 | Location | Utility area is located at right side exterior. |
| 1651 | Floor | Serviceable. Carpet of concrete. |
| 1652 | Walls & Ceiling | Serviceable. Wafer board. |
| 1653 | Doors | Suggestion. See exterior doors at item 1113 for additional information. |
| 1654 | Windows | None. |
| 1655 | Cabinets | None. |
| 1656 | Electrical | Suggestion. Light fixture at ceiling would not function at time of inspection. Possible spent bulb. Suggest review prior to closing. |
| 1657 | Utility Room Comments | None. |

CRAWLSPACE

The crawlspace review is visual and the area is entered if safely possible. The crawlspace area was inspected using a standard flashlight and a small probe.

Water seepage and moisture penetration are common problems in crawlspaces usually resulting from inadequate water management above ground.  Improving drainage and grading can correct most causes.  Our review of the crawlspace cannot always detect the past or future possibility of water in this area.  We suggest that you obtain disclosure from the prior occupants regarding any history of water in the crawlspace and obtain price estimates when infiltration is disclosed or signs of water are present.  NOTE: The presence of a sump pump can suggest water has or may enter the crawlspace. Moisture in a crawlspace can promote wood decay, therefore crawlspaces should be adequately ventilated and vents should be left open year round.

| Step # | Component | Comments |
| --- | --- | --- |
| 1801 | Access | Serviceable. Crawlspace was accessed unless noted otherwise in this section. |
| 1802 | Floor | Suggestion. Dirt. Floor area damp in several areas from condensation from ductwork. See item 1815 for additional information. |
| 1803 | Subfloor | Serviceable. Plywood. |
| 1804 | Walls | Serviceable. Brick, concrete block. |
| 1805 | Floor Joists | Recommendation. 2 x 10. Some Mold noted on joists at center rear and center front. This is an indication that joists have been wet or the crawlspace environment is damp. Client should keep crawlspace vents open to maximize ventilation. Recommend annual review to ensure crawlspace remains dry and the current mold growth is not increasing. If client is concerned suggest review by a qualified specialist |
| 1806 | Support Posts/Columns | Serviceable. Concrete block, brick. |
| 1807 | Beams | Serviceable. Wood. |
| 1808 | Windows | None. |
| 1809 | Electrical | Serviceable. |
| 1810 | Insulation | Recommendation. Rolled fiberglass insulation approximately 4-6 inches. Insulation is missing, loose and hanging down at several locations. Recommend re-installing by a Qualified Specialist. |
| 1811 | Ventilation | Serviceable. Screened vents. |
| 1812 | Vapor Barrier | Serviceable. Plastic. |
| 1813 | Sump Pit | None. |
| 1814 | Plumbing | Serviceable. |
| 1815 | HVAC Ducts | Suggestion. Sheet metal. Ducts are not insulated. This may have been acceptable at time of construction, however due to condensation observed on ductwork insulation is suggested for increase energy efficiency. |
| 1816 | Dryer Vent | Serviceable. Metal duct. |
| 1817 | Down Draft Cook top Vent | None. |
| 1818 | Crawlspace Comments | Recommendation. Wood scraps noted at several locations throughout crawlspace. Recommend removing all wood scraps and debris from crawlspace. |

HEATING & A/C – MAIN UNIT

The inspection of the heating & AC system is not a 'Code Compliance' inspection nor are 'Manufacturer's Specifications' for installation, operation or repairs a part of this inspection.  Code compliance and manufacturer's specifications on any product/component or item should be verified through the local building authorities, the company who manufactured the item or product, or with seller prior to closing. The visual review of the duct system is limited. Ducts in walls, under insulation or otherwise obstructed from view are not within the scope of this inspection.

| Step # | Component | Comments |
| --- | --- | --- |
| 1901 | Heating | Serviceable. Unit is located at crawlspace; fuel is gas, forced air, gas shut off and electrical shutoff noted. Filter size 16 x 25 x 1 (at unit in crawlspace.) |
| 1902 | Conditions | Serviceable. |
| 1903 | Exhaust Venting | Serviceable. |
| 1904 | Thermostat | Serviceable. Thermostat located at hall. |
| 1905 | Ducting | Serviceable. Flex and sheet metal duct. |
| 1906 | Air Conditioning System | Serviceable. Electric, condenser and compressor unit is located at rear exterior, electrical disconnect provided at equipment. This is a split system. The air conditioner was activated to check the operation of the motor and the compressor and both appeared to be in serviceable condition. A detailed review of the cooling capacity of this unit is beyond the scope of this inspection. We make no warranty as to the system's adequacy. |
| 1907 | A/C Temperature Differences | Serviceable. The air temperature was measured at the supply and return registers for the main unit. The difference between these two temperatures should be in the range of 14-22 degrees F when the A/C system is functioning properly. The supply temperature was 60F and the return air temperature was 76F. The difference in air temperature was 14F. |
| 1908 | Heating & A/C Comments | Manufacture date on compressor is 4/98. Unit is older and client should plan on replacing/upgrading system in future. |

PLUMBING

Shut off valves/angle stops under kitchen/bathroom sinks and toilets are not turned or tested during the inspection due to the possibility of causing leaks.  All shut off valves/angle stops should be turned regularly by the homeowner to ensure free movement in case of emergency. The plumbing supply, drains, waste, and vent piping materials are only visible in the attic, crawlspace and basement areas (if present) and at interior fixture locations. Material identification was based upon visible piping in these areas.

| Step # | Component | Comments |
| --- | --- | --- |
| 2001 | Plumbing Supply System | Suggestion. Property is connected to a public system. Water shutoff at street. Water shut off not observed in home and shutoff handle is missing to valve in crawlspace. Suggest review shutoff location with owner or Licensed Plumber for repairs if needed. |
| 2002 | Plumbing Waste System | Serviceable. Property is connected to a public waste system. |
| 2003 | Supply Pipes | Serviceable. Copper. |
| 2004 | Drain, Waste & Vent Pipes | Suggestion. PVC, Cast iron and galvanized. Galvanized waste pipes rust from the inside of the pipe and cane become restricted over time. When slow waste water flow is noted some restriction may have occurred. Flow appeared normal unless otherwise noted in this report. If concerned, suggest review by a Plumber. |
| 2005 | Ejector Pump | None. |
| 2006 | Water Heater | Suggestion. Estimated 38-gallon capacity, located in cabinet at laundry room…Cold water shut off valve is installed and a temperature/pressure relief valve is installed as a safety feature. Hot water was noted at all tested plumbing fixtures indicating the electric water heater elements were functioning properly at the time of inspection. These elements are not visible or accessible to the inspector and are not tested at the time of inspection. These elements can fail at any time without warning. No warranty, guarantee or certification is given as to future failures. Limited review due to Cabinet installed around unit. |
| 2007 | Water Temperature | Serviceable. The hot water temperature was measured at a faucet during the inspection and was observed to be 117F. The U.S. Consumer Product Safety Commission (CPSC) urges all users to lower their water heater temperature settings to 120F to reduce or eliminate the risk of most tap water scald injuries. Client is advised that a 120F setting may not provide adequate hot water for all clothing and dish washing machines and a higher setting may be required. Suggest lowering the hot water temperature to the lowest setting that will satisfy the hot water needs and protect against scald injuries due to the elevated water temperature observed |
| 2008 | Water Heater Exhaust Venting System | None. |
| 2009 | Sump Pit | None. |
| 2010 | Cross Connections | None. |
| 2011 | Plumbing System Comments | None. |

ELECTRICAL SYSTEM

| Step # | Component | Comments |
| --- | --- | --- |
| 2101 | Electrical Main Box | Serviceable. The main panel is located at rear exterior and the sub panel is located at laundry room and garage. The main electrical service is approximately 100 amps and 220 volts. Service entrance is underground. Overload protection is provided by breakers. Main disconnect noted. Main conductor is aluminum. Low amperage (15 & 20 amp) branch circuit conductor is copper. Visible wiring type is non metallic sheathed. Evidence suggests system is properly grounded. |
| 2102 | Additional Main Panel Comments | Recommendation. Double lugging noted at exterior rear panel left side 30 amp breaker. This can add to the load of the affected circuits causing a possible overload and tripping of the breakers. This is a safety concern. Damaged/loose hinges on exterior panel. Recommend review by a Licensed Electrician for repairs as needed to ensure safety. |
| 2103 | General System Comments | Suggestion. Duke energy may own the exterior panel and they maintain any panel it owns. Client should review all of this information with Duke Power by calling 800-777-9898. |
| 2104 | Smoke Detectors | Recommendation. Smoke detector(s) located at hall. When smoke detectors are installed client is advised that Underwriters Laboratories (UL) states that smoke detectors usually should be replaced after 10 years of service if electric and after 5 years of service if battery-run. The inspector is not able to determine age of installed unit(s). Suggest review with owner regarding date of installation. Periodic testing is suggested to ensure proper operation. Suggest installing additional smoke detectors throughout the home as needed for safety. Smoke detector inoperable at hall. Recommend replacing smoke detector. |
| 2105 | Carbon Monoxide Detector | None. Suggest installing carbon monoxide detectors throughout the home as needed for safety. |
| 2106 | Electrical System Comments | Suggestion. Alarm system noted. Suggest review with alarm contractor. |

KITCHEN/BREAKFAST

The kitchen inspection is a combination of visual and operational testing. Appliances are operated (if power is supplied) using normal operating controls.  Calibrations to cooking systems or their efficiencies are not evaluated nor are life expectancies given.  NOTE:  Dishwashers can fail at any time due to their complexity.  Our review is to determine if the system is free of leaks and excessive corrosion.

| Step # | Component | Comments |
| --- | --- | --- |
| 2301 | Floor | Serviceable. Vinyl. |
| 2302 | Walls | Serviceable. Painted |
| 2303 | Ceiling | Serviceable. |
| 2304 | Doors | Serviceable. |
| 2305 | Windows | Serviceable. |
| 2306 | Electrical | Suggestion. No ground fault circuit interrupter (GFCI) noted. GFCI protection not required when home was built. GFCI is a safety device that the buyer may wish to install |
| 2307 | Heat Source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 2308 | Counter Tops | Serviceable. Laminate |
| 2309 | Cabinets | Serviceable. |
| 2310 | Sinks | Serviceable. |
| 2311 | Faucets | Recommendation. Hand Sprayer leaks. Recommend replacing hand sprayer to prevent damage under sink. Recommend maintenance/repair by Licensed Plumber. |
| 2312 | Traps/Drain System | Serviceable. |
| 2313 | Disposal | Serviceable. Appliance Brand: insinkerator/ISE. |
| 2314 | Dishwasher | Recommendation. Appliance Brand: Kenmore. Dishwasher was tested using normal operating controls. Unit functioned properly at time of inspection. Dishwashers most commonly fail internally at the pump, motor or seals. These units are not disassembled to inspect these components nor are they visible or accessible to the inspector. Our inspection is limited to operating the unit on the 'normal wash' cycle only. Grinding noise noted at startup of pump. Unit is not secured to cabinet. Recommend maintenance/repair by a Qualified Specialist. |
| 2315 | Stove/Cook Top/Oven | Recommendation. Electric. Appliance Brand Kenmore. The electrical stove/range elements were tested at the time of inspection and appeared to function properly. These can fail at any time without notice. No warranty, guarantee or certification is given as to future failure. Handle is loose. Unit is not secured with an anti tip device. This may not have been required at time of installation. Recommend Qualified Specialist install anti tip device for safety. |
| 2316 | Oven-Separate Unit | Recommendation. Appliance Brand: GE. The electrical stove/range elements were tested at the time of inspection. These can fail at any time without notice. No warranty, guarantee or certification is given as to future failure. Oven bake element would not heat properly. Recommend maintenance/repair by a Qualified Specialist. |
| 2317 | Hood/Fan | Serviceable. Vented to exterior. |
| 2318 | Microwave | None. Free standing unit property of owner. |
| 2319 | Trash Compactor | None. |
| 2320 | Ceiling Fan | None. |
| 2321 | Kitchen Comments | None. |

INTERIORS

Review of the interior areas of walls, columns, chimney chases and the areas between ceilings and the flooring above are not possible. These areas may contain piping, electrical wires, ducts, structural components and other systems. This inspection is visual and non-destructive. By definition any area that is not accessible is not visible. Therefore these areas are excluded from this report.

| Step # | Component | Comments |
| --- | --- | --- |
| 2351 | Comments | Wood floors. Most gaps in floors are normally caused by seasonal fluctuations in humidity- the floor expands from high humidity and contracts during periods with low humidity. This type of expansion and contraction is considered to be normal and expected for solid wood floors. In solid wood floors, gaps may be the thickness of a dime (1/32) or wider. Wider boards may have even wider gaps. Square edged floors show gaps more than beveled floors, and light colored floors show gaps more than darker colored floors. Recommendation. Several Baseboard electrical heat units /thermostats throughout home are inoperable/or disconnected. Recommend review of all baseboard heat by a Licensed Electrician if client plans on using this system. |

DINING ROOM

| Step # | Component | Comments |
| --- | --- | --- |
| 2401 | Floor | Serviceable. Carpet. |
| 2402 | Walls | Serviceable. Painted. |
| 2403 | Ceiling | Serviceable. |
| 2404 | Doors | Serviceable. |
| 2405 | Windows | Serviceable. |
| 2406 | Electrical | Serviceable. |
| 2407 | Heat Source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 2408 | Fireplace | None. |
| 2409 | Ceiling Fan | None. |
| 2410 | Dining Room Comments | None. |

LIVING ROOM

| Step # | Component | Comments |
| --- | --- | --- |
| 2501 | Floor | Serviceable. Carpet. |
| 2502 | Walls | Serviceable. Painted. |
| 2503 | Ceiling | Serviceable. |
| 2504 | Doors | Serviceable. |
| 2505 | Windows | Serviceable. |
| 2506 | Electrical | Serviceable. |
| 2507 | Heat Source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 2508 | Fireplace | None. |
| 2509 | Ceiling Fan | None. |
| 2510 | Living Room Comments | None. |

FAMILY ROOM

| Step # | Component | Comments |
| --- | --- | --- |
| 2601 | Floor | Serviceable. Carpet. |
| 2602 | Walls | Serviceable. Papered. |
| 2603 | Ceiling | Serviceable. |
| 2604 | Doors | Recommendation. Door is loose and will not latch to hall. Recommend maintenance/repair by a Licensed General Contractor. |
| 2605 | Windows | Serviceable. |
| 2606 | Electrical | Serviceable. |
| 2608 | Heat Source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 2609 | Fireplace | Serviceable. . Masonry fireplace. Gas log installed. Pilot was lit and unit was turned on. Unit appeared to function properly. Damper locked open with metal clip for safety when logs are in use. |
| 2610 | Ceiling Fan | Serviceable. |
| 2611 | Wet Bar | None. |
| 2612 | Family Room Comments | None. |

ENTRY

| Step # | Component | Comments |
| --- | --- | --- |
| 2701 | Floor | Serviceable. Tile. |
| 2702 | Walls | Serviceable. Painted, papered. |
| 2703 | Ceiling | Serviceable. |
| 2704 | Doors | Serviceable. |
| 2705 | Windows | Serviceable. Fixed. |
| 2706 | Electrical | Serviceable. |
| 2707 | Heat Source | Suggestion. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 2708 | Entry Comments | None. |

HALLS/STAIRS

| Step # | Component | Comments |
| --- | --- | --- |
| 2800 | Location | Located at 1st and 2nd story at center of home. |
| 2801 | Floor | Serviceable. Wood. |
| 2802 | Walls | Serviceable. Painted. |
| 2803 | Ceiling | Serviceable. |
| 2804 | Doors | Serviceable. |
| 2805 | Electrical | Serviceable. |
| 2806 | Stairs | None. |
| 2807 | Railing | None. |
| 2808 | Whole House Fan | Serviceable. Unit functioned at time of inspection. |
| 2809 | Comments | None. |

BATHROOM - MASTER

Our focus in bathrooms is directed at identifying visible water damage and/or visible plumbing problems.  We may not always mention common faults such as stuck stoppers or dripping faucets.  If considered important, you should check these items independently.  Minor cosmetic issues such as common rust, corrosion and stains may not always be reported.

| Step # | Component | Comments |
| --- | --- | --- |
| 3000 | Location | Bathroom is located at left rear. |
| 3001 | Floor | Serviceable. Vinyl. |
| 3002 | Walls | Serviceable. Papered. |
| 3003 | Ceiling | Serviceable. |
| 3004 | Doors | Recommendation. Door will not latch. Recommend maintenance/repair by a Licensed General Contractor. |
| 3005 | Windows | None. |
| 3006 | Electrical | Suggestion. No ground fault circuit interrupter (GFCI) noted. GFCI protection not required when home was built. GFCI is a safety device that the buyer may wish to install |
| 3007 | Heat Source | Serviceable. Forced air register observed. Electrical heat unit installed at ceiling functioned at time of inspection. |
| 3008 | Exhaust Fan | Serviceable. |
| 3010 | Tub/Surround | None. |
| 3011 | Tub Enclosure | None. |
| 3012 | Tub Faucet | None. |
| 3013 | Shower/Surround | Serviceable. Shower surround. Tile. Common cracks noted. The shower pan and accessible surrounding areas were visually inspected for leaks. No visual leaks noted at time of inspection. Shower pans are not filled and tested for leaks during the inspection |
| 3014 | Shower Door | Suggestion. No safety glass observed. Safety glass may not have been used at time of installation. Suggest review with Qualified glass company to install safety glass. |
| 3015 | Shower Faucet | Serviceable. |
| 3016 | Sink | Serviceable. |
| 3017 | Sink Faucet | Serviceable. |
| 3018 | Traps/Drain Supply | Serviceable. |
| 3019 | Toilet | Serviceable. |
| 3020 | Counter/Cabinets | Serviceable. |
| 3021 | Spa Tub | None. |
| 3022 | Bathroom Comments | None. |

BATHROOM #2 HALL

| Step # | Component | Comments |
| --- | --- | --- |
| 3000.2 | Location | Hall. |
| 3001.2 | Floor | Serviceable. Tile. |
| 3002.2 | Walls | Serviceable. Papered. |
| 3003.2 | Ceiling | Serviceable. |
| 3004.2 | Doors | Serviceable. |
| 3005.2 | Windows | None. |
| 3006.2 | Electrical | Suggestion. No ground fault circuit interrupter (GFCI) noted. GFCI protection not required when home was built. GFCI is a safety device that the buyer may wish to install |
| 3007.2 | Heat Source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 3008.2 | Exhaust Fan | Suggestion. Fan motor is noisy and may need to be replaced in future. |
| 3010.2 | Tub/Surround | Recommendation. Porcelain tub and tile. Bathtubs are not filled to test the overflow valves for leaks at the time of inspection due to time consumption and waste of water. This is a visual inspection only for stains or other signs of leaks. Many leaks are concealed and not visible to the inspector at the time of inspection. No visible leaks noted at time of inspection, though leaks may occur at anytime without warning. No guarantee, warranty or certification is given as to future leaks. Cracked caulk and grout was noted. Recommend all tile edges and tub/shower walls be caulked and sealed to prevent moisture penetration. All damaged caulk and grouting should be replaced. Failure to keep walls sealed can cause deterioration and extensive moisture damage to the interior walls and sub-flooring. This damage is not always visible or accessible to the inspector at the time of inspection. |
| 3011.2 | Tub Enclosure | None. |
| 3012.2 | Tub Faucet | Serviceable. Shower head noted. |
| 3013.2 | Shower/Surround | None. |
| 3014.2 | Shower Door | None. |
| 3015.2 | Shower Faucet | None. |
| 3016.2 | Sink | Serviceable. |
| 3017.2 | Sink Faucet | Serviceable. |
| 3018.2 | Traps/Drain Supply | Recommendation. Tub drains slowly. Recommend maintenance/repair by a Licensed Plumber. |
| 3019.2 | Toilet | Serviceable. |
| 3020.2 | Counter/Cabinets | Serviceable. |
| 3021.2 | Spa Tub | None. |
| 3022.2 | Bathroom Comments | None. |

BEDROOM MASTER

| Step # | Component | Comments |
| --- | --- | --- |
| 3200 | Location | Bedroom is located at left rear. |
| 3201 | Floor | Serviceable. Wood. |
| 3202 | Walls | Serviceable. Painted. |
| 3203 | Ceiling | Serviceable. |
| 3204 | Doors | Serviceable. |
| 3205 | Windows | Serviceable. |
| 3206 | Electrical | Serviceable. |
| 3207 | Heat source | Serviceable. Forced air register observed. Baseboard electrical unit noted. |
| 3208 | Closets/Wardrobe | Serviceable. |
| 3209 | Fireplace | None. |
| 3210 | Ceiling Fan | Serviceable. |
| 3211 | Comments | None. |

BEDROOM #2 CENTER FRONT

| Step # | Component | Comments |
| --- | --- | --- |
| 3200.2 | Location | Center front. |
| 3201.2 | Floor | Serviceable. Carpet. |
| 3202.2 | Walls | Serviceable. Painted. |
| 3203.2 | Ceiling | Serviceable. |
| 3204.2 | Doors | Serviceable. |
| 3205.2 | Windows | Recommendation. Locking hardware inoperable. Recommend repairs as needed by a Licensed General Contractor to secure window. . |
| 3206.2 | Electrical | Serviceable. |
| 3207.2 | Heat source | Suggestion. Forced air register observed. Baseboard electrical unit noted. See item 2351 at interiors for additional information. |
| 3208.2 | Closets/Wardrobe | Serviceable. |
| 3209.2 | Fireplace | None. |
| 3210.2 | Ceiling Fan | Serviceable. |
| 3211.2 | Comments | None. |

BEDROOM #3 LEFT FRONT

| Step # | Component | Comments |
| --- | --- | --- |
| 3200.3 | Location | Left front. |
| 3201.3 | Floor | Serviceable. Carpet. |
| 3202.3 | Walls | Serviceable. Painted. |
| 3203.3 | Ceiling | Serviceable. |
| 3204.3 | Doors | Serviceable. |
| 3205.3 | Windows | Recommendation. Top sash drops at front. Recommend repairs as needed by a Licensed General Contractor |
| 3206.3 | Electrical | Serviceable. |
| 3207.3 | Heat source | Serviceable. Forced air register observed. Baseboard electrical unit noted. |
| 3208.3 | Closets/Wardrobe | Serviceable. |
| 3209.3 | Fireplace | None. |
| 3210.3 | Ceiling Fan | Serviceable. |
| 3211.3 | Comments | None. |

BEDROOM #4 CENTER REAR

| Step # | Component | Comments |
| --- | --- | --- |
| 3200.4 | Location | Right. |
| 3201.4 | Floor | Serviceable. |
| 3202.4 | Walls | Serviceable. |
| 3203.4 | Ceiling | Serviceable. |
| 3204.4 | Doors | Serviceable. |
| 3205.4 | Windows | Serviceable. |
| 3206.4 | Electrical | Serviceable. |
| 3207.4 | Heat source | Serviceable. Forced air register observed. Baseboard electrical unit noted. |
| 3208.4 | Closets/Wardrobe | Serviceable. |
| 3209.4 | Fireplace | None. |
| 3210.4 | Ceiling Fan | Serviceable. |
| 3211.4 | Comments | None. |

# Text boxes

6/20/2011